## Slide 1: Research Question
Optimal (kinematic?) design of manipulator to detect early stresses in Greenhouse Crops
פגישת מאסטר:
תאריך: 10.11.2019
נוכחים: עמי, אביטל, תמיר

## Slide 2: Manipulator
Joints : can be Prismatic, Roll, Pitch
All links are cylindrical
The Z axe is always in the long part of the cylinder
The plant presented as cylinder: R=0.5m H=0.75m
The manipulator format: URDF
Each manipulator combination described as the following:
Joint Type-> Axe according parent coordinate system -> link length
Example: Roll_Z_0.1–Pitch_Z_0.4–Roll_Y_0.7-Pris_Y_0.4 -Pris_X_0.1
The Camera orientation isn’t important  5DOF  add to all the manipulators a Roll joint along Z Axe after the last link
To Simulate the mobile Platform I add Prismatic Joint which parallel to the plant

## Slide 5: Links Weights
Take links length & weight from 2 different manipulators: (UR5 & Motoman NXC100)
Get the ratio between the accumulated weight and accumulated length
* Weight[i] = acc_length[i] * 8.79 + 4.29 –acc_weight[i-1]

## Slide 6: Indices
Notes: -
-
-

## Slide 7: Manipulator Optimization
Objectives:
Min. Degrees of Freedom\ Degree of Redundancy [3 - 6 \ -3 – 0]
Min. Cycle Time [0-10]
Max manipulability\ Local Conditioning index [0-1]
Min z (Mid-Range Proximity) [0 -?]
Independent variables :
X1 : Joints Types: array [Roll, Pitch, Yaw]
X2: Previous axe : array [X , Y, Z]
X3: Links Lengths: array [0.1 ,0.4, 0.7] (meters)
X4: Number Degrees of Freedom: Int [3, 4, 5, 6]
Notes: In order to find the optimal manipulator I am using ROS and Gazebo as simulator.
The Objectives of the optimization is to find the manipulator, with min. DOF and min cycle time, that can reach to all desired detection points.
The independent variables: DOF, Joints Types, joints sequence and links lengths.
- This gives me over 2 billion combinations, so some assumptions must be done:

## Slide 8: Manipulator Optimization (cnt’d)
Assumptions \ Constrains:
First joint is rotational along Z axe: X1[0] = Roll, X2[0] = Z
First link length = 0.1m : X3[0]=0.1
Total length of all the links > 1m : Sum (X3) > 1
2 adjacent prismatic joints must be perpendiculars
No more than 3 prismatic joints
After Roll joint can’t be Roll\Pitch joint in the Z axe: If X1[i]==Roll and (X1[i+1]==Roll or X1[i+1]==Pitch) than X2[i+1]!=Z
After Roll Joint or the following joints sequence [ Roll -> Pris Z] the next joint wont be in the X axe: if (X1[i]==Roll or (X1[i-1]==Roll and X1[i]== Pris and X2[i] == Z)) than X2[i+1]!=X
Joints limits: for Roll\ Pitch [0-360°] and for Pris [0 – 2*link length]
Number Points of Detection: 4 -- Success :need to reach to one of the 2 top points and to the middle and the lower points

## Slide 9: להמשך:
הכנסת התוצאות שיש כרגע מהסימולציה לאלגוריתם קיים (3-NSGA / MOEA\D) לקבלת תחושה/ תוצאות ראשונות
פיתוח אלגוריתם לאופטימיזציה
הכנסת תוצאות הסימולטור לאלגוריתם לימוד מכונה (SVM/NN) למידול ההתנהגות – יוכל להחליף חלקית את הסימולטור לצורך האצת האופטימיזציה

## Slide 10: פגישת מאסטר: תאריך: 26.11.2019 נוכחים: עמי, אביטל, תמיר
נקודות ממפגש קודם
בדיקת קשר בין המדדים שהוצגו
הכנת טבלת קונספטים – יתבצע דיון עלייה היום

## Slide 11: Simulation
עד כה ביצעתי סימולציה על 126,841 זרועות מתוך 1,695,044 זרועות אפשריות7.5%))
מתוך 126,841 זרועות כ- 9597 זרועות הוגדרו כהצלחה (7.5%)

## Slide 12: Indices
נראה שיש קשר בין LCI ל MANIPULABILITY
JOINT MID גדל במספר דרגות חופש גדולות

## Slide 13: Time Compression
נראה שהזמן לא יכול להוות מדד מדויק

## Slide 14: Concepts
 |  |  | Concepts |  |  |  |  |  |  |  |  | 
 | Variable | number of concepts | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | DOF | 4 | 3 | 4 | 5 | 6 | *** | *** | *** | *** | *** | ***
2 | Pitch joints | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
3 | Long links (0.7 m) | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
4 | about y axe | 5 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | *** | ***
5 | acc length | 5 | 1-1.5 | 1.6-2 | 2.1-2.6 | 2.7-3.1 | 3.1-3.6 | *** | *** | *** | *** | ***
6 | # of parallel axes | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
7 | Type | 4 | Cartesian | Cylindrical | Polar | articulated | *** | *** | *** | *** | *** | ***
8 | longest link | 2 | 0.4 | 0.7 | *** | *** | *** | *** | *** | *** | *** | ***
9 | prismatic to revolute ratio | 10 | 0 | 0.2 | 0.25 | 0.33 | 0.5 | 0.67 | 1 | 1.5 | 2 | 3
10 |  |  |  |  |  |  |  |  |  |  |  | 
 | total | 64240 |  |  |  |  |  |  |  |  |  | 

## Slide 15: פגישת מאסטר: תאריך: 09.12.2019 נוכחים: עמי, אביטל, תמיר
נקודות ממפגש קודם
התאמת כל קונפיגורציה לקונספט מתאים
נרמול מדד MID RANGE PROXIMITY
ביצוע סינון של קונספטים - BRUTE FORCE : לקחת אחוז מסויים מכל קונספט ולראות אם הוא מספיק/מספק ומצורה זו לבחור כמה קונספטים שיחקרו לעומק

## Slide 16: Indices - updated
נראה שיש קשר בין LCI ל MANIPULABILITY

## Slide 17: Concepts - updated
 |  |  | Concepts |  |  |  |  |  |  |  |  | 
 | Variable | number of concepts | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | DOF | 4 | 3 | 4 | 5 | 6 | *** | *** | *** | *** | *** | ***
2 | Pitch joints | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
3 | Long links (0.7 m) | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
4 | about y axe | 5 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | *** | ***
5 | acc length | 5 | 1-1.5 | 1.6-2 | 2.1-2.6 | 2.7-3.1 | 3.1-3.6 | *** | *** | *** | *** | ***
6 | # of parallel axes – y | 5 | 0 |  | 2 | 3 | 4 | 5 | *** | *** | *** | ***
7 | # of parallel axes – z | 4 | 0 |  | 2 | 3 | 4 |  | *** | *** | *** | ***
8 | longest link | 2 | 0.4 | 0.7 | *** | *** | *** | *** | *** | *** | *** | ***
9 | prismatic to revulote ratio | 10 | 0 | 0.2 | 0.25 | 0.33 | 0.5 | 0.67 | 1 | 1.5 | 2 | 3
 | Total | 11588 |  |  |  |  |  |  |  |  |  | 

## Slide 18: Concepts
יש מספר פחות קונספטים ממה שרשום בטבלה מכיוון שיש קשר בין חלק מהקונספטים
מצאתי 794 קונספטים עם לפחות קונפיגורציה אחת
כל קונספט מכיל בין 1-68520 קונפיגורציות

## Slide 19: דברים אחרים
לוודא קבלת אביטל כמנחה

## Slide 20: Concepts - updated
Concepts |  |  |  |  |  |  |  |  |  | 
 | Variable | number of concepts | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | DOF | 3 | 4 | 5 | 6 | *** | *** | *** | *** | ***
2 | Pitch joints | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | ***
3 | Long links (0.7 m) | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | ***
4 | acc length | 5 | 1-1.5 | 1.6-2 | 2.1-2.6 | 2.7-3.1 | 3.1-3.6 | *** | *** | ***
5 | # of parallel axes – y | 5 | 0 | 2 | 3 | 4 | 5 | *** | *** | ***
6 | longest link | 2 | 0.4 | 0.7 | *** | *** | *** | *** | *** | ***
7 | prismatic to revulote ratio | 8 | 0 | 0.2 | 0.25 | 0.33 | 0.67 | 1 | 1.5 | 3
 | total | 794 |  |  |  |  |  |  |  | 

## Slide 21: פגישת מאסטר: תאריך: 03.02.2020 נוכחים: עמי, אביטל, תמיר
נקודות ממפגש קודם
פיתוח אלגוריתם גנטי לשלב ב': חיפוש אבולוציוני עם גישת DWOI
ביצוע סימולציה לכל הקונספטים הקטנים (220 קונפיגורציות – הורחב גם לכל 5 דג"ח)
לבניית DWOI ראשוני להשתמש בכל התוצאות שיש
אביטל התקבל להיות מנחה

## Slide 23: Concepts in WOI

## Slide 24: GA

## Slide 25: GA
גודל אוכלוסייה- לכל קונספט לפי הגודל אבל לא משתנה תוך כדי
התאמה – לפי מרחק –
סלקציה – רולטה
מוטציות – שינוי איברים בצורה מעגלית מהורה אקראי (40%)
קרוסאובר – בחירת איבר רנדומלי והחלפה עד איבר זה מהורה אחד ומאיבר זה מהורה שני (60%) - מה קורה אם לא מצליח לייצר צאצא?
אליטיזם – בכל קונספט ישמר ארכיב בגודל האוכ' של התוצאות הכי טובות

## Slide 26: GA
תנאי עצירה:
מקומי: עבור קונספט
כל האוכלוסייה / אחוז מסוים ממנה נבדק
תלוי בהקצאת משאבים
לא מצליח לייצר יותר צאצאים?
גלובלי: כל הריצה
מספר דורות
זמן ריצה
כמות מסוימת של קונספטים בחזית