## Slide 1: Research Question
Optimal (kinematic?) design of manipulator to detect early stresses in Greenhouse Crops
פגישת מאסטר:
תאריך: 10.11.2019
נוכחים: עמי, אביטל, תמיר

## Slide 2: Manipulator
Joints : can be Prismatic, Roll, Pitch
All links are cylindrical
The Z axe is always in the long part of the cylinder
The plant presented as cylinder: R=0.5m H=0.75m
The manipulator format: URDF
Each manipulator combination described as the following:
Joint Type-> Axe according parent coordinate system -> link length
Example: Roll_Z_0.1–Pitch_Z_0.4–Roll_Y_0.7-Pris_Y_0.4 -Pris_X_0.1
The Camera orientation isn’t important  5DOF  add to all the manipulators a Roll joint along Z Axe after the last link
To Simulate the mobile Platform I add Prismatic Joint which parallel to the plant

## Slide 5: Links Weights
Take links length & weight from 2 different manipulators: (UR5 & Motoman NXC100)
Get the ratio between the accumulated weight and accumulated length
* Weight[i] = acc_length[i] * 8.79 + 4.29 –acc_weight[i-1]

## Slide 6: Indices
Notes: -
-
-

## Slide 7: Manipulator Optimization
Objectives:
Min. Degrees of Freedom\ Degree of Redundancy [3 - 6 \ -3 – 0]
Min. Cycle Time [0-10]
Max manipulability\ Local Conditioning index [0-1]
Min z (Mid-Range Proximity) [0 -?]
Independent variables :
X1 : Joints Types: array [Roll, Pitch, Yaw]
X2: Previous axe : array [X , Y, Z]
X3: Links Lengths: array [0.1 ,0.4, 0.7] (meters)
X4: Number Degrees of Freedom: Int [3, 4, 5, 6]
Notes: In order to find the optimal manipulator I am using ROS and Gazebo as simulator.
The Objectives of the optimization is to find the manipulator, with min. DOF and min cycle time, that can reach to all desired detection points.
The independent variables: DOF, Joints Types, joints sequence and links lengths.
- This gives me over 2 billion combinations, so some assumptions must be done:

## Slide 8: Manipulator Optimization (cnt’d)
Assumptions \ Constrains:
First joint is rotational along Z axe: X1[0] = Roll, X2[0] = Z
First link length = 0.1m : X3[0]=0.1
Total length of all the links > 1m : Sum (X3) > 1
2 adjacent prismatic joints must be perpendiculars
No more than 3 prismatic joints
After Roll joint can’t be Roll\Pitch joint in the Z axe: If X1[i]==Roll and (X1[i+1]==Roll or X1[i+1]==Pitch) than X2[i+1]!=Z
After Roll Joint or the following joints sequence [ Roll -> Pris Z] the next joint wont be in the X axe: if (X1[i]==Roll or (X1[i-1]==Roll and X1[i]== Pris and X2[i] == Z)) than X2[i+1]!=X
Joints limits: for Roll\ Pitch [0-360°] and for Pris [0 – 2*link length]
Number Points of Detection: 4 -- Success :need to reach to one of the 2 top points and to the middle and the lower points

## Slide 9: להמשך:
הכנסת התוצאות שיש כרגע מהסימולציה לאלגוריתם קיים (3-NSGA / MOEA\D) לקבלת תחושה/ תוצאות ראשונות
פיתוח אלגוריתם לאופטימיזציה
הכנסת תוצאות הסימולטור לאלגוריתם לימוד מכונה (SVM/NN) למידול ההתנהגות – יוכל להחליף חלקית את הסימולטור לצורך האצת האופטימיזציה

## Slide 10: פגישת מאסטר: תאריך: 26.11.2019 נוכחים: עמי, אביטל, תמיר
נקודות ממפגש קודם
בדיקת קשר בין המדדים שהוצגו
הכנת טבלת קונספטים – יתבצע דיון עלייה היום

## Slide 11: Simulation
עד כה ביצעתי סימולציה על 126,841 זרועות מתוך 1,695,044 זרועות אפשריות7.5%))
מתוך 126,841 זרועות כ- 9597 זרועות הוגדרו כהצלחה (7.5%)

## Slide 12: Indices
נראה שיש קשר בין LCI ל MANIPULABILITY
JOINT MID גדל במספר דרגות חופש גדולות

## Slide 13: Time Compression
נראה שהזמן לא יכול להוות מדד מדויק

## Slide 14: Concepts
 |  |  | Concepts |  |  |  |  |  |  |  |  | 
 | Variable | number of concepts | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | DOF | 4 | 3 | 4 | 5 | 6 | *** | *** | *** | *** | *** | ***
2 | Pitch joints | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
3 | Long links (0.7 m) | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
4 | about y axe | 5 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | *** | ***
5 | acc length | 5 | 1-1.5 | 1.6-2 | 2.1-2.6 | 2.7-3.1 | 3.1-3.6 | *** | *** | *** | *** | ***
6 | # of parallel axes | 6 | 0 | 1 | 2 | 3 | 4 | 5 | *** | *** | *** | ***
7 | Type | 4 | Cartesian | Cylindrical | Polar | articulated | *** | *** | *** | *** | *** | ***
8 | longest link | 2 | 0.4 | 0.7 | *** | *** | *** | *** | *** | *** | *** | ***
9 | prismatic to revolute ratio | 10 | 0 | 0.2 | 0.25 | 0.33 | 0.5 | 0.67 | 1 | 1.5 | 2 | 3
10 |  |  |  |  |  |  |  |  |  |  |  | 
 | total | 64240 |  |  |  |  |  |  |  |  |  | 

## Slide 15: דברים אחרים
לוודא קבלת אביטל כמנחה